## Slide 1: Site Closure Presentation For Department of Ecology Consideration
Whittaker SKS Site PPCD #13-2-27556

## Slide 2: Prepared by – Aspect consulting
Dave Cook, LG, CPG
Principal Geologist
206.838.5837 : dcook@aspectconsulting.com
Ali Cochrane, LG
Associate Geologist
206.949.7478 : acochrane@aspectconsulting.com
Baxter Call, EIT
Project Engineer
206.369.7652 : bcall@aspectconsulting.com
On behalf of– LMI - West Seattle, LLC (aka GID)
Elton Lee
Vice President, Asset Management- GID
415.495.3003 : elee@gid.com

## Slide 3: Presentation goals
Summarize current and historical environmental conditions on the Site
Show basis for empirical demonstration of compliance as stated in WAC-173-340-747
Provide information in support of formal requests for:
  Certificate of Completion and Closure of Site #6015
  Delisting from the Hazardous Sites List
  Close out of PPCD No. 13-2-27556-2
    Removal from the Hazardous Sites List
    Dismissal of the PPCD at King County Superior Court

## Slide 4: Agenda
Project Timeline and Milestone Recap
Compliance Monitoring Site Conditions
Compliance Groundwater Monitoring Results
Empirical Demonstration of Compliance
Site Closure

## Slide 5: Project Milestones

## Slide 6
Project Milestones
On-Property excavation of petroleum-contaminated soil
Dewatering of petroleum-contaminated groundwater
Original well network:
11 compliance groundwater wells
4 repurposed dewatering wells (the “RW” wells)
The “RW” wells showed persistent DRO above Method A CUL
Pilot study indicated well system and formation not suitable for injections
The “RW” wells replaced with proper compliance well, MW115
Quarterly compliance monitoring focuses on MW115
2015 Construction & Remedial Excavation Completed
January 2021 Pilot Study for in-situ Treatment
January 2022 Replace Dewatering Wells with Compliance Well
March 2016 to December 2020 Quarterly Compliance GWM
March 2022 to June 2023 Resume Compliance GWM
Late 2023 Request Site Closure from Department of Ecology
DRO = diesel-range organics
CUL = cleanup level
GWM = groundwater monitoring

## Slide 7: Compliance monitoring site conditions

## Slide 8
Pictured groundwater elevation contours from November 2012.
Historically, groundwater flow to North-Northeast following West Seattle’s natural gradient.
Pre-construction groundwater flow

## Slide 9
Post-Construction groundwater flow
Pictured groundwater elevation contours from Q4 2022 compliance monitoring event.
Since construction was completed, localized groundwater flow has been reversed.
Now flows South-Southwest towards footing drain.

## Slide 10
FINAL EXCAVATION LIMITS – NE PROPERTY CORNER
Photograph from Cleanup Action Report, SKS Shell Station Site, 3901 Southwest Alaska Street, Seattle, Washington, dated October 20, 2016

## Slide 11
Compliance monitoring site map
  10 compliance monitoring wells shown in blue
  Cross sections depict existing soil conditions at remedial excavation boundaries.
  There is an estimated 500 yd3 of DRO and GRO contaminated soil remaining in the vadose zone capped under Fauntleroy Way, and SW Alaska St ROW.

## Slide 12
Fauntleroy way right-of-way Cross section

## Slide 13
Alaska street right-of-way Cross section

## Slide 14: Compliance Groundwater Monitoring Data

## Slide 15
Groundwater Monitoring Data
As of Q2 2019, all wells show COCs below MTCA Method A
Except RW03 and RW04 (dewatering, extraction wells): showed persistent diesel-range TPH above Method A
Decommissioned & replaced with MW115 in Q1 2022

## Slide 16
Groundwater Monitoring Data
Four consecutive quarters below MTCA. Other Site COCs have been ND or below MTCA Method A cleanup levels in all MW115 sampling events
Chart: Diesel-Range TPH Results
| 44645 | 44833 | 44910 | 45000 | 45093
MW115 | 780 | 220 | 190 | 140 | 210
Method A Cleanup Level | 500 | 500 | 500 | 500 | 500

## Slide 17: Diesel-range TPH Results
Groundwater Monitoring Data
7 Consecutive Quarters Below MTCA
4 Consecutive Quarters Below MTCA

## Slide 18: Compliance Groundwater Data Summary
MW115 has 4 consecutive quarters of results below MTCA Method A cleanup levels
All other existing wells (9) in network have at least 7 consecutive quarters of results below MTCA Method A cleanup levels for all Site COCs

## Slide 19: Empirical demonstration of compliance

## Slide 20: Case for empirical demonstration
Requirements for Empirical Demonstration1 | Case for Empirical Demonstration at SKS Whittaker Site | Requirement Met?
The measured groundwater concentration is less than or equal to the applicable groundwater cleanup level2. | Entire compliance monitoring well network has at least four consecutive quarters of results below cleanup levels. | 
The measured soil concentration will not cause an exceedance of the applicable groundwater cleanup level2 at any time in the future. | Sufficient time has passed for migration of hazardous substances from soil into groundwater to occur. | 
 | The characteristics of the site are representative of future site conditions, and owner has no intention to change site use. | 
 | Residual soil contamination exists only in the vadose zone and is not in direct contact with groundwater. | 
1As stated in WAC 173-340-747 (9)(b)
2Established under WAC 173-340-720

## Slide 21
Compliance Monitoring at downgradient Wells
  MW104, MW108, MW109, and MW110 are directly downgradient of, and closest to, residual soil contamination.
  All have at least 7 consecutive quarters of compliance monitoring data below MTCA Method A CULs for all Site COCs.

## Slide 22
MW104 Compliance groundwater trend
Groundwater Elevation
Benzene
Gasoline-Range TPH
Diesel-Range TPH

## Slide 23
MW108 compliance groundwater trend
Groundwater Elevation
Benzene
Gasoline-Range TPH
Diesel-Range TPH

## Slide 24
MW109 compliance groundwater trend
Groundwater Elevation
Benzene
Gasoline-Range TPH
Diesel-Range TPH

## Slide 25
MW110 compliance groundwater trend
Groundwater Elevation
Benzene
Gasoline-Range TPH
Diesel-Range TPH

## Slide 26: Proposed next steps

## Slide 27: Proposed Next Steps
Prepare and submit Site Closure request, late 2023
Submit a Prospective Purchaser Consent Decree close out letter to Ecology, and request a Certificate of Completion, late 2023
Decommission remaining Site monitoring wells, early 2024
Work with the AGO to dismiss the PPCD in King County Superior Court, early 2024
Delisting the Site from the Hazardous Sites List, early 2024

## Slide 28: Questions?